## Slide 1
EMAP DATASET CHALLENGE
Predicting Arousal from EEG Topomaps with a CNN + Bi-LSTM Ensemble
Scalp topomaps from the 64-channel band-power features, a model for within-trial change, and a small ensemble.
Submitter: Shreejay Subedi Mentor: Dr. Saurav K. Aryal
IEEE CEC 2026
64-channel EEG · 4 frequency bands · 4 peripheral signals

## Slide 2
Approach
Each 0.5-second bin has 64 EEG channels with 4 band powers each, plus 4 peripheral signals. We lay the 64x4 EEG values out as a 24x24 picture of the scalp using the standard 10-20 electrode positions (mne-python) and inverse-distance interpolation between electrodes.
Two branches per bin:
  A small 2-D CNN reads the scalp picture and produces a 64-dim embedding.
  An MLP reads the raw 260 features plus per-band statistics, short differences of the peripheral signals, and where the bin sits in its trial.
The two branches are added and passed through a 2-layer bidirectional LSTM, then a linear head outputs arousal (clipped to [0,1]).
One model is trained to predict only the within-trial change (arousal minus the trial average) so it can focus on the moment-to-moment shape; the average is added back at prediction time.
A loop-quartile feature marks which of the 4 video repetitions a bin belongs to. On its own it lowered a model from 0.3126 to 0.3045 in a single-change test.
A larger 48x48 topomap was used for the within-trial model; the weight search preferred it over the 24x24 version.
Final arousal prediction: a weighted average (weights fit on validation) of three models, then light per-trial smoothing and a small variance correction.
Heart rate and GSR are predicted separately by gradient-boosted models, each with feature selection (a univariate F-test filter and LightGBM gain importance). The target is never used to predict itself.
selected_features.csv lists the features chosen for each target. Selection did not hurt accuracy and helped arousal slightly (0.3158 to 0.3123 with the boosted model).
Code: prediction.py, model.py, model_v2.py, model_assets/, training_code/

## Slide 3
Results — 29 held-out participants, 696 trials, 84,019 bins
Regression — three targets (RMSE)
Target | RMSE | Mean-pred
Arousal | 0.3055 | 0.323
Heart rate (BPM) | 9.42 | 9.41
GSR | 1.0e-5 | 1.0e-5
Arousal beats the mean baseline; HR and GSR sit at it. Across 4 algorithms x 5 feature views (~34 models), best HR R2 = 0.02 and GSR R2 = 0 — the 0.5-s averages keep little fast dynamics. Arousal path: mean 0.3226, LightGBM 0.3150, CNN+Bi-LSTM 0.3111, ensemble 0.3055.
Classification (low vs high at 0.5)
F1 binary
0.6609
F1 macro
0.5980
Accuracy
0.6020
Feature selection: a univariate F-test filter and LightGBM gain importance, applied per target. Kept 80 (arousal), 43 (HR), 80 (GSR) of 264 features; listed in selected_features.csv.
Where the error comes from
We split the error into the trial mean (overall level) and the within-trial shape: RMSE² ≈ trial_mean² + within_trial². On validation that is 0.264 and 0.155, which matches the 0.306 total.
The within-trial part is near its limit here. Our best within-trial model reaches 0.154, and ensembling did not improve it.
Most of the error is in the trial mean. A constant, ridge and boosted models on trial summaries, a per-subject context model, and a transformer over all 24 of a participant’s trials all landed near 0.27, about the level of guessing the global average.
Given the true trial means, our within-trial predictions would reach about 0.15 RMSE, so the remaining error is almost entirely in the trial mean.
That overall level seems to sit in the raw EEG waveform, which is averaged out when each 0.5 s window becomes four band-power numbers.